## Slide 1: Implementation Oriented Mutation Testing of Statechart Models
Mark Trakhtenbrot
Holon Institute of Technology
markt@hit.ac.il

## Slide 2: Challenges in development of reactive systems
Main problem: complex behavior - Intricate event-driven interaction with the environment - Concurrency - Timing factors Typically: Critical applications (embedded RT controllers, …) Must fulfill tough requirements (safety, timeliness, … )

## Slide 3: Apply formal methods
Model-based development: statecharts to capture behavior; a renown standard
executable model; a basis for automated tools (simulation, model checking)
model-level analysis (closer to problem domain, ignore implementation details,
earlier detection of errors)
mutation testing: shift from program level to model level

## Slide 4
Example: Rail Cross Control
No_train
Train_in
Train_coming / Close
Sensors
Train_leaving / Open
Close / Bar_down
Open / Bar_up
Ack_down
Ack_up
Monitor
Fix
Dly 5
Dly 5
Opened
Wait_
down
Closed
Error
Wait_
up
Break
Fix
Barrier
Damaged
U_moving
Opened
D_moving
Closed
Bar_down
Bar_up
D_done /
Ack_down
U_done /
Ack_up

## Slide 5: Statecharts mutation testing
So far: focus on language specific mutations
S. Fabbri et. al. :
coverage criteria to assess the test set quality (all configurations, all transitions, all broadcastings)
- delete transition, change broadcast source / target, etc.
M.Trakhtenbrot [Mutation 2007]:
- address hierarchy

## Slide 6: Common for all analysis tools (simulation, model checking, mutation testing)
- Strictly follow the language semantics
- Ignore potential behavioral differences between
system model and its actual implementation
But why any difference can occur at all?
- Due to abstractions assumed by the modeling language

## Slide 7: Core abstractions in statecharts
Maximal parallelism: enabled transitions (and relevant actions) in all components are taken simultaneously, in one step
Step execution doesn’t take time: system completes its reaction before the next external event occurs
Events are active during one step only: broadcasted when generated, no buffering
Immediate reaction to expired time delay by the awaiting component

## Slide 8: And in the real world…
Maximal parallelism ?
Statechart components are mapped into concurrent tasks;
ready tasks are executed in some order
Step execution doesn’t take time ?
Every single action takes some real time, according to its “weight”
Events are active during one step only ?
Queued to avoid their loss
Immediate reaction to expired time delay?
Awaiting task will run after delay’s expiration, according to the scheduling policy

## Slide 9: How this affects the tests adequacy?
Implementation:
- Allows for scenarios that are impossible in the model
- Test set developed for the model might be not adequate anymore…
Two approaches:
- Find what is missing when the system is implemented. Too late!
- Instead, consider and analyze model mutants that address the mentioned differences. (M.T. in [Mutation 2007])
Need clear distinction between two types of tests adequacy:
- Model level
- Implementation-oriented

## Slide 10: New mutations and what they address
Adequacy with respect to real time
- Increasing delay duration
- Making reactions “take time”
Adequacy related to concurrency
- Interleaving enforcement (for transitions and actions)
Problems addressed:
- Reaction not completed before arrival of next external event
- Events missed due to time glitches
- Racing between concurrent components

## Slide 11: Mutation of timeouts duration
S
dly(T)
P
S
dly(T+Δ)
P

## Slide 12
Rail Cross Control - mutating delay duration
If control is returned to task Monitor in more than 5 sec,
then it might miss event Fix
Close / Bar_down
Open / Bar_up
Ack_down
Ack_up
Monitor
Fix
Dly 5+Δ
Dly 5
Opened
Wait_
down
Closed
Error
Wait_
up

## Slide 13: Enforcement of transitions interleaving
Maximal parallelism:
transitions executed simultaneously
E
E
E
S1
S2
P2
P1
Q2
Q1
E/E2
E2/E3
E3
Q2
Q1
P2
P1
S1
S2
Mutant:
serialization of transitions

## Slide 14
Rail Cross Control – interleaving enforcement
Close / Bar_down
Open / Bar_up
Ack_down
Ack_up
Monitor
Fix / Fix1
Dly 5
Dly 5
Opened
Wait_
down
Closed
Error
Wait_
up
Break
Fix1
Barrier
Damaged
U_moving
Opened
D_moving
Closed
Bar_down
Bar_up
D_done /
Ack_down
U_done /
Ack_up
Monitor
concludes that the barrier is fixed and opened before the barrier actually returned to its OPENED state

## Slide 15: Transition with actions that “take time”
S1
S2
P1
P1
/ ak+1;…;an
S1
S2
dly (Δ(
E1
E1
E/a1;…;ak
E / a1;a2;…;an
Transition with all actions executed in “zero time”
Mutant: now it takes time to arrive to S2
Yet another way to cause interleaving

## Slide 16: OS scheduler
Idle
Priority_
ready
add_job_to_RQ / compute_job_priority -- formula
/ insert_into_RQ_according_to_priority -- search
Wait_job
Created
new_job / create_PCB -- fill record
/ add_job_to_RQ -- send message
Wait_
CPU_news
Got_job_data
preempt_request / get_CPU_job
/ add_job_to_RQ
Got_job_to_run
[empty_CPU & non_empty_RQ] / get_RQ_head
/ send_job_to_CPU
Wait_for_update
idle_over /
update_priorities_in_RQ
RQ handler
Running handler
RQ_age_handler
New job handler

## Slide 17: What is caused by this mutation
Idle
Priority_
ready
add_job_to_RQ / compute_job_priority
/ insert_into_RQ_according_to_priority -- search
Wait_for_update
dly (age_slice) /
update_priorities_in_RQ
RQ handler
RQ_age_handler
While RQ_handler is executing a series of actions called
insert_into_RQ_according_to_priority
(after mutation it takes time!)
…
RQ_age_handler may start performing
update_priorities_in_RQ
Was impossible in the original model; reveals a W-W racing

## Slide 18: Selection of mutants
Knowledge needed to generate mutants:
Analysis of the model only
Enforce transitions interleaving
Enforce serialization of actions on the same transition
Analysis of test execution traces
Enforce serialization of actions on concurrent transitions:
If transitions T1 and T2 were executed in the same step,
then check whether their actions are in potential racing
If yes, create a mutant in which execution of T1 (or T2) is delayed
All these lead to generation of relatively few mutants

## Slide 19: Selection of mutants
Utilize info about the environment
Expected exec time for actions in the modeling language
Scheduling policy
Example: in mutation of delay duration assume
N components in the statechart
Round-Robin scheduling of obtained tasks
The most “heavy” transition requires exec time H
Then task awaiting for dly D might get control only after the time
ACT_D= D + (N-1)*H.
Heuristic: generate 2 mutants
with dly (ACT_D) and dly (ACT_D/2)

## Slide 20: Selection of mutants
More considerations:
Local vs. global mutations:
- In each mutant, only one transition “takes time”
(transitions with “heavy” actions are good candidates)
- All transitions “take time”
(probably the best approximation,
if proper actions’ weights are taken)

## Slide 21: Further steps
Implementation of the mutation operators Further study and implementation of methods for efficient generation of mutants Experimentation (manual, and based on implementation)

## Slide 22: Thank you!

## Slide 23: OS scheduler – making actions “take time” Same “execution time” for all actions
Wait_job
Created
/ add_job_to_RQ -- send message
New job handler
Dly (Δ)
new_job / create_PCB
-- fill record
Wait_job
Created
new_job / create_PCB -- fill record
/ add_job_to_RQ
-- send message
New job handler
Dly (Δ)

## Slide 24: OS scheduler – making actions “take time” “Execution time” depends on type of action
Wait_job
Created
new_job / create_PCB -- fill record
/ add_job_to_RQ
-- send message
New job handler
Dly (msg_Δ)

## Slide 25: OS scheduler – making actions “take time” All actions in the model take time - this mutant provides a better approximation to implementation - involves a global change in the model
Wait_job
Created
new_job / create_PCB
-- fill record
/ add_job_to_RQ
-- send message
New job handler
Dly (msg_Δ)
Dly (fill_rec_Δ)